## Slide 1: D-RATS
Dan Smith - KK7DS
MicroHAMS Digital Conference 2009

## Slide 2: Outline
What is D-STAR?
What is D-RATS?
  Goal
  Messaging
  Files and Images
  Positional Awareness
  Future
Implementation

## Slide 3: What is D-STAR?
Purely digital mode
Simultaneous voice and data
High-speed (DD) and Low-speed (DV)‏
Repeater and gateway infrastructure
All DV radios can do ~950bps data
  No modem required
  Just a serial port (no framing, ECC, etc)‏
  Not 8-bit safe

## Slide 4: What is D-RATS (Goal)‏
All-in-one tool for D-STAR data ops
Provide real uses for data channel
Oriented at EmComm
No dependence on infrastructure
  Originally targeted for simplex
  All network interaction at endpoints

## Slide 5: What is D-RATS? (Messaging)‏
Free-form multicast chat messages
  Checksum-protected
  No ACK/NAK from remote stations (yet)‏
Structured messages
  Use XML to convey structure and content
  XSL at the endpoints for presentation
Email gateway
  Crafted headers for reply and forward

## Slide 6: What is D-RATS? (Files and Images)‏
Arbitrary file transfers with sliding window, compression, and resume
“File server” for remote retrieval
Integrated image resize/resample

## Slide 7: What is D-RATS? (Positional Awareness)‏
Captures and sends ICOM GPS strings
Distance and direction calculation
Integrated map display
External GPS to multiplex the port
Moving stations updated in real-time

## Slide 8: What is D-RATS? (Future)‏
Move to more BBS-centric behavior
  Email-client-like messaging interface
  FTP-client-like file transfer interface
  Better event capture and logging
Mapping improvements
  Modules for display of various POIs
  Performance
  Usability

## Slide 9: Implementation
Written in Python/GTK
Runs on Linux, Mac, and others.
Full session stack protocol
OpenStreetMap.org for free maps

## Slide 10: References
D-RATS Website
  http://www.d-rats.com
D-RATS Mailing List
  http://lists.danplanet.com

## Slide 11
Notes: http://www.microhams.com
Created by Scott N7SS

## Slide 12: Backup