## Slide 1
D-RATS
Dan Smith - KK7DS
SeaPac 2009

## Slide 2: Outline
What is D-STAR?
What is D-RATS?
  Goal
  Messaging
  Files and Images
  Positional Awareness
  Network Connectivity
Implementation

## Slide 3: What is D-STAR?
Purely digital mode
Simultaneous voice and data
High-speed (DD) and Low-speed (DV)‏
Repeater and gateway infrastructure
All DV radios can do ~950bps data
  No modem required
  Just a serial port (no framing, ECC, etc)‏
  Not 8-bit safe

## Slide 4: What is D-RATS (Goal)‏
All-in-one tool for D-STAR data ops
Provide real uses for the slow data channel
Oriented at EmComm
No dependence on infrastructure
  Originally targeted for simplex
  All network interaction at endpoints

## Slide 5: What is D-RATS? (Changes in 0.3)‏
Improved User Interface
Provide more BBS-like behavior (still at endpoints!)‏
  Email-client-like messaging interface
  FTP-client-like file transfer interface
  Better event capture and logging
  Email transport of forms (interface with WinLink)‏
Mapping improvements, dynamic data, speed
Multiple data ports (multiple radios, networks)‏

## Slide 6: What is D-RATS? (Messaging)‏
Free-form multicast chat messages
  Checksum-protected
  No ACK/NAK from remote stations (yet)‏
Structured messages
  Use XML to convey structure and content
  XSL at the endpoints for presentation
Email gateway
  Crafted headers for reply and forward
  Ad-hoc setups at the end points (no infrastructure)‏

## Slide 12: What is D-RATS? (Files and Images)‏
Arbitrary file transfers with sliding window, compression, and resume
“File server” for remote retrieval
Integrated resize/resample of image files

## Slide 14: What is D-RATS? (Positional Awareness)‏
Captures and sends ICOM GPS strings
Distance and direction calculation
Integrated map display
External GPS to multiplex the port
Moving stations updated in real-time
Free maps!

## Slide 20: What if I don't have D-STAR?

## Slide 21: Ratflector
Connect to other D-RATS users via Internet
Easy and clean for testing
Data-only reflector
Configure D-RATS serial port for:
  net:ref.d-rats.com:9000
Anyone can set one up for private or public use

## Slide 22: TNC – The gateway drug to D-STAR data
Use a KISS-mode TNC with D-RATS
Gives you point-to-point data transfer
No AX.25
  Simpler to setup
  Lower overhead
Interface with D-STAR users through stations running both formats

## Slide 23: Implementation
Written in Python/GTK
Runs on Linux, Mac, and Windows
Full session stack protocol
OpenStreetMap.org for free maps

## Slide 24: References
D-RATS Website
  http://www.d-rats.com
D-RATS Mailing List
  http://lists.danplanet.com